## Slide 1: 13.2 Evaluation of EarthCARE/CPR simulation and preparation for data assimilation in the global NWP system of JMA
Kozo OKAMOTO1
E. Oikawa1, I. Okabe1, R. Shimizu2, T. Tanaka3, and T. Kubota3 1:JMA/MRI, 2:RESTEC, 3:JAXA/EORC
Notes: Session 13 – Data Assimilation and Orographic Rainfall (13:30 – 14:30)
13:45-14:00

## Slide 2: Background and Objectives
Cloud Profiling Radar (CPR)
  CloudSat/CPR (Apr 2006~ Dec 2023), EarthCARE/CPR (May 2024~)
  Have enhanced our understanding of cloud process and improved NWP/climate models
Assimilation of CPR
  Limited study: Small coverage, Challenges in model simulation and data assimilation processings
  Unique info that passive obs does not have: Vertically resolved cloud/precipitation
  Operational implementation at ECMWF (June 2026)
    Fielding & Janisková 2020; Janisková & Fielding 2020, ECMWF 2026
Objectives of this study
  Investigate feasibility of assimilation of EarthCARE/CPR reflectivity (Z) in JMA’s global system
Degrade
Improve
Forecast error change at day 4 for wind vector @ECMWF
Notes:   https://www.ecmwf.int/en/about/media-centre/news/2026/earthcare-cloud-radar-data-world-first
  CloudSat/CPR
    NASA-CSA, 2006.4~
    94.05GHz, sampling 1100m(H),250m(V), min. detectable lev:-28dBZ
  EarthCARE/CPR
    JAXA-NICT, 29 May 2024
    94.05GHz, sampling 500m(H),100m(V), 解像度 1km or 10km(H), 500m(V) min. detectable level:-35dBZ
    Measure vertical Doppler velocity
Previous studies
Understand cloud processes, evaluate and improve NWP models
Barker 2008; Delanoe et al. 2011; Jiang et al. 2012; Di Michele et. al. 2012; Suzuki et al. 2015; Kawai et al. 2014
Understand climate processes and evaluate and improve earth system models
Jiang et al. 2012; Su et al. 2013; McCoy et al. 2015, Kawai et al. 2015; Suzuki et al. 2015; Koshiro et al. 2018
Challenges in DA
Sensitive to cloud microphysics and overlap assumption
High nonlinearity, Zero-gradient issue for cloudy obs but clear-sky model simulation
Fielding & Janisková 2020; Janisková & Fielding 2020
EarthCARE launch: 29 May 2024
EarthCARE/CPR vs CloudSat/CPR
衛星高度 393km vs 705km
解像度 0.65 x 1km (H)x 500m(V) vs 1.4 x 3.5 km(H) x 500m(V)
https://space.oscar.wmo.int/instruments/view/cpr_earth_care
https://space.oscar.wmo.int/instruments/view/cpr_cloudsat
7dBZの感度向上 => 5倍の感度
10^-2.8/10^-3.5 ~ 5.0

## Slide 3: Content
1. Comparison of obs and simulation (background)
2. Initial test of assimilation
3. Preparation for advanced data assimilation

## Slide 4: Model, Simulator and Observation
Model: Global Spectral Model (GSM): JMA’s operational model (JMA 2026)
  Horizontal spacing of 13km, 128 layers up to 0.01 hPa
  Convection scheme： Prognostic Arakawa-Schubert  Convective clouds
  Large-scale cloud: Smith scheme (Smith 1990, QJRMS)  Stratus clouds
  Hydrometeor: cloud water+ice, rain flux, snow flux
Simulator: RTTOV ver13.0
  Optical parameters of cloud water, cloud ice, rain and snow (Geer 2021, AMT)
  Calculate attenuated reflectivity factor (Z), and its Jacobian
  The same fraction for all hydrometeors
Observations: EarthCARE/CPR L2A CPR_ECO
  version vBa, 10km integration data
  Create super-ob (~55 km based on 4DVar inner-loop scale) by averaging reliable data
    Vertically thin every other bin (~dH=200 m)
    Select reliable data over -30 dBZ, integrated_radar_reflectivity_flag_10km=0, and SNR>-10 [dB]
    Remove mirror-echo-flagged bins and multiple-scattering-flagged columns
Notes: vAc:
vAe: Jan.2025, +2.4dBZ
vBa: Mar.2025, +1.6dBZ, mirror echo+multiscattering
SNRの単位は dBZではなくdBであることに注意

## Slide 5: (Preliminary) Quality Control (QC)
Reliability
  Both observed and simulated Z ≥ -30 dBZ
  Higher than 1km in altitude to avoid ground clutter
Homogeneity
  Standard Deviation < 20 dBZ, cloud fraction > 50 % and effective data number (Npix) > 5
    These statistics are calculated from effective data composing a super-ob
Consistency btw obs and sim
  |Obs-Sim| < 24 dBZ
Notes: O-Bcheckのしきい値はもっと厳しくする？
現在は 50dBZになっているが、ECでは20dBZ
ECでのQC
・cloud fraction > 0.2 for bath obs and model
閾値が緩すぎる： too loose, too lenient, too permissive
閾値が粗すぎる： too coarse, too crude, not fine enough
閾値が厳しすぎる： too strict, too tight, too severe
・

## Slide 6: Example of obs and simulation for CPR Z [dBz]
12UTC, 3 Aug, 2024
Obs (original)
Obs (super-ob)
Sim (GSM)
Sim (GSM) after QC
Obs (super-ob) after QC

## Slide 7: 2D-histogram in Z and Height
3-24 Aug. 2024
Simulation underestimates Z above 10 km
  GSM underestimates high clouds (Okamoto et al. 2021, QJRMS)
-35 Z [dBZ] 0 10 25
-35 Z [dBZ] 0 10 25
-35 0 25 [dBZ]
Height [km]
0 5 10 15
Obs
Sim (GSM BG)
Obs-Sim (O-B)
Notes: cpr10p10k

## Slide 8: 2D-histogram in Z and Temperature
Simulation underestimates Z below -40 deg C and overestimates above 0 deg C
What cause these biases?
Obs
Sim (GSM BG)
Obs-Sim (O-B)
Temperature [deg C]
20
0
-40
-20
-60
-30 0 20 Z[dBZ]
-30 0 20 Z[dBZ]
-30 0 20 Z[dBZ]
Notes: cpr10p10k

## Slide 9: Investigate bias sources
Narrow down causes of the bias: obs, RTTOV, super-ob, sampling,,,
  Use more reliable cloud input (AC_CLP=CPR+ATLID) instead of GSM cloud
  Compare 1km obs and simulation from RTTOV and AC_CLP
    Classify cloud ice (water) into snow and cloud ice (rain and cloud water) according to particle radius and size distribution
However, strange peak in simulation around 5 dBz, and consistent negative O-B
  Issues with AC_CLP (cloud water) and/or its scattering calculation in RTTOV?
Obs
Sim (AC_CLP)
Obs-Sim
Notes: 11-24 Aug. 2024

## Slide 10: Content
1. Comparison of obs and simulation (background)
2. Initial test of assimilation
3. Preparation for advanced data assimilation

## Slide 11: Assimilation of CPR reflectivity
Adapt the global 4D-Var to assimilate Z
Initial test based on single analysis: 00UTC 11 Aug, 2024
Global DA
  JMA’s operational system as of 2026 (JMA 2025) + all-sky IR (geo)
  Hybrid 4DVar (incremental 4DVar + LETKF)
    Inner-loop (55km) + Outer-loop (13km)
    Cloud is not directly analyzed but adjusted by other variables (TQWP) through the linearized forecast model and outer-loop update
  Updated O-B at the 2nd outer-loop (O-B2) is used to see how Z assimilation adjust analysis variables and then forecast of clouds
Note: Preliminary setting
  Preliminary QC thresholds, fixed obs error (7dBz) and no vertical correlation, no bias correction

## Slide 12: QC-passed data
2024.8/11.00UTC
  8/10.21UTC-8/11.03UTC)
Thinning H80km-V200m
QC-passed O-B (dBZ)
9km(51L)
6km(66L)
12km(36L)
2km(86L)
Notes: O-B2, 20

## Slide 13: Analysis difference of CPR and noCPR
T [K]
CWC [g/1000kg]
TTD [K]
U [m/s]
850hPa
700hPa
T [K]
CWC [g/1000kg]
TTD [K]
U [m/s]
Notes: anl_p: cpr- nocpr: ECPRB_04517007- 04517006, 2024081100

## Slide 14: C.Pac
Negligible change by CPR assimilation
OB
BG
nocpr, O-B2
cpr, O-B2
O-B1

## Slide 15: S.Ocean
Slightly better fit than background (O-B1) and No-CPR (O-B2)
OB
BG
nocpr, O-B2
cpr, O-B2
O-B1

## Slide 16: Content
1. Comparison of obs and simulation (background)
2. Initial test of assimilation
3. Preparation for advanced data assimilation

## Slide 17: Vertical correlation for obs and O-B
Correlation for obs/O-B at 10 km height
Large vertical correlation length
  Distance with corr <0.2 is 5 km (obs) and 6.5km (O-B)
 Need larger thinning distance and/or accounting for vertical error correlation
0.0 0.2 0.4 0.6 0.8 [corr]
0 1 2 3 [Num*10,000]
0.0 0.2 0.4 0.6 0.8 [corr]
0 1 2 3 [Num*10,000]
Obs
O-B
land
ocean
land —
ocean —
Notes: grid間隔 500m(H),100m(V), 解像度 1km or 10km(H), 500m(V)

## Slide 18: Vertical correlation for obs and O-B
Correlation for obs/O-B at 5 km height
Large vertical correlation length
  Distance with corr <0.2 is 4.5 km (obs) and 5.5km (O-B)
 Need larger thinning distance and/or accounting for vertical error correlation
0.0 0.2 0.4 0.6 0.8 [corr]
0 1 2 3 [Num*10,000]
0.0 0.2 0.4 0.6 0.8 [corr]
0 1 2 3 [Num*10,000]
O-B
Obs
land —
ocean —
land —
ocean —
Notes: grid間隔 500m(H),100m(V), 解像度 1km or 10km(H), 500m(V)

## Slide 19: Summary and plans
Examine reflectivity simulation using the global DA system
  Generally well reproduced observation, but underestimated (overestimate) below -40 deg C (above 0 deg C)
  Simulation with AC_CLP and RTTOV shows strange peak at 5dBz and consistent overestimation (O-S<0)
Initial check of Z assimilation with preliminary setting
  Single analysis suggests small but reasonable impacts
Advanced data assimilation processing is under development
  Vertical error correlation should be accounted for
Plans
  Investigate bias sources and sensitivity to optical parameters in more detail
  Short cycle experiments after initial checks
  Develop cloud-dependent QC, obs error, and BC
Notes: L2 (single sensor) products will be open to the public in March 2025

## Slide 20: Supplemental slides

## Slide 21: AC_CLP  RTTOV input
粒径に応じて雲氷（雲水）を、氷・雪（雲水・雨）に分類
  0/1の分類ではなく、粒径分布に基づき割合も考慮
Small particles
()
Large particles
()
Large particles
()
Small particles
()
Cloud ice
Snow
Cloud water
Rain
Altitude [km]
Cloud ice [g m－3]
Cloud water [g m－3]
Time [hour, UTC]
Time [hour, UTC]
4 hydrometer types used in RTTOV
AC_CLP cloud product

## Slide 22: Cloud effect parameter and obs error in DA
Cloud effect parameter is a key to all-sky radiance (ASR) assimilation
  Cloud effect parameter for IR ASR: CA = (|O-Bclr| + |B-Bclr| )/2 (Okamoto et al. 2014)
    O: observation, B: all-sky simulation, B:clear-sky simulation, defined in brightness temperature [K]
  O-B standard deviation (SD) models used as obs error model (Geer and Bauer 2011; Okamoto et al. 2023, 2034)
Apply ASR’s CA to CPR Z
  CPR’s CA = (O+B)/2 + Bclr [dBZ], Sclr=-35dBZ
  O-B normalized by the obs model shows Gaussian form
EarthCARE/CPR Z
O-B SD
O-B mean
sample num
Obs Error model (quadratic fitting)
Log(num)
O-B SD and mean [dBZ]
0 10 20 30 40 50 60
CA[K]
O-B/SDall
O-B/SDca
Norm Gauss
O-B/SDca
O-B/SDall
-6 -4 -2 0 2 4 6
Normalized O-B
EarthCARE/CPR Z

## Slide 23: Dependence of PSD and particle shape
Particle size distribution (PSD)：
Marshall-Palmer distribution (MPD),
Field et al. 2007 (PSD-F07T:tropical, PSD-F07M:midlatitude),
Modified gamma distribution (MGD)
－ MGD-W ()
－ MGD-Rnew ()
Large column aggregate
(LCA)
Eriksson et al. 2018
8-column aggregate
(8CA)
 | Rain | Snow | Cloud water | Cloud ice
Standard | Sphere, MPD | LPA, PSD-F07T | Sphere, MGD-W | LCA, PSD –F07T
Rnew | Sphere, MGD-Rnew | LPA, PSD-F07T |  | 
Snew | Sphere, MPD | 8CA, PSD-F07M |  | 
Rnew+Snew | Sphere, MGD-Rnew | 8CA, PSD-F07M |  | 
Large plate aggregate
(LPA)
MGD

## Slide 24: Dependence of PSD and particle shape
Altitude [km]
Reflectivity [dBZ]
Altitude [km]
Reflectivity [dBZ]
Reflectivity [dBZ]
Reflectivity [dBZ]
Reflectivity [dBZ]
obs－sim(STD)
obs－sim(Rnew)
obs－sim(Snew)
obs－sim(Rnew+Snew)
obs(1km)
sim(Rnew）
sim(STD）
sim(Snew）
sim(Rnew+Snew）