## Slide 1
Overview of Passive Microwave Missions at EUMETSAT for Precipitation Monitoring
V. Barlakas1, C. Accadia1, V. Mattioli1, J. Ackermann1, T. Hewison1, F. De Angelis1, S. Di Michele1, I. Krizek1, R. Ekelund1, J. Lu2, D. Ori2, F. Lemmouchi2
1EUMETSAT, Eumetsat-Allee 1, 64295 Darmstadt, Germany
2CS Group Germany, Robert-Bosch-Straße 7, 64293 Darmstadt
12th Workshop of International Precipitation Working Group, July 7-10, 2026, Kraków, Poland

## Slide 2
EPS-SG MW and sub-mm wave missions
MWS, MWI and ICI
CIMR at EUMETSAT
EUMETSAT activities in support of CIMR mission
EPS Sterna
Precipitation products at a glance

## Slide 3
courtesy of ESA
Metop-SG A
Metop-SG B
MicroWave Sounder (MWS)
Microwave Imager (MWI)
Ice Cloud Imager (ICI)
Courtesy of ESA
Launched on 13 August 2025
EPS Second Generation (EPS-SG) Program
To be launched in 2026
Orbit: Sun-synchronous polar at ~835 km
Coverage: 14 orbits/day (orbital period ~100 min)
Carries multiple instruments, including two MW imagers and a sounder
Conical scanners (53°±2°) with a 1700 km swath
Cross-track scanner (±49.85°) with a ~2250 km swath
Notes: There will be three satellite pairs, where each satellite will have a nominal lifetime of 7.5 years to span a total operational lifetime over 21 years

## Slide 4
courtesy of ESA
Courtesy of ESA
EPS Second Generation (EPS-SG) Program
MicroWave Sounder | MicroWave Imager | Ice Cloud Imager
Main applications: Spectral radiance measurements on Temperature Water vapour profiles Cloud liquid and cirrus detection | Main applications: Cloud and precipitation products | Main applications: First operational radiometer for ice cloud monitoring Non-precipitating ice - not covered either in the optical and thermal IR or in the mm-wave range
For Numerical Weather Prediction: Nowcasting and very short-range forecasting Support NWP at regional and global scales | For Numerical Weather Prediction: Nowcasting and very short-range forecasting at regional scales Support NWP at regional and global scales | For climate monitoring: Ice cloud products Validation of ice cloud models Parameterisation of ice clouds in weather and climate models
For climate monitoring: Temperature and humidity sounding records | For climate monitoring: Continuity of key microwave channels as observed by SSM/I, TMI, SSMIS, AMSR-E, GMI | 
For surface measurements: Observations of sea ice and snow cover, surface temperature, and emissivity | For surface measurements: Observations of sea ice parameters and snow cover, snow water equivalent, sea surface wind | 
Notes: There will be three satellite pairs, where each satellite will have a nominal lifetime of 7.5 years to span a total operational lifetime over 21 years

## Slide 5: MicroWave Sounder (MWS)
Channel | Frequency (GHz) | Footprint (IFOV) Size at 3dB (km)
MWS-1 | 23.8 | 40
MWS -2 | 31.4 | 40
MWS -3 | 50.3 | 20
MWS -4 | 52.8 | 20
MWS-5 | 53.246  0.08 | 20
MWS -6 | 53.596  0.115 | 20
MWS-7 | 53.948  0.081 | 20
MWS -8 | 54.40 | 20
MWS -9 | 54.94 | 20
MWS -10 | 55.50 | 20
MWS -11 | 57.290344 | 20
MWS-12 | 57.290344  0.217 | 20
MWS-13 | 57.290344 0.32220.048 | 20
MWS-14 | 57.2903440.32220.022 | 20
MWS-15 | 57.2903440.32220.010 | 20
MWS-16 | 57.2903440.32220.0045 | 20
MWS-17 | 89.0 | 17
MWS-18 | 165.5 ± 0.725 | 17
MWS-19 | 183.311  7.0 | 17
MWS-20 | 183.311  4.5 | 17
MWS-21 | 183.311  3.0 | 17
MWS-22 | 183.311  1.8 | 17
MWS-23 | 183.311  1.0 | 17
MWS-24 | 229  GHz | 17
Ch. 1 – 2: Total Column Water Vapor (TCWV)
Ch. 1 – 3: Sea-ice, land surface temperature
Ch. 1 – 3 & 17 – 18: Ice Water Path (IWP), precipitation
Ch. 24: Cirrus cloud detection
24 channels (23.8 – 229 GHz)
Spatial resolution: ~40 km at low freqs., ~17 km at high freqs.
Temperature & humidity sounding, surface, cloud ice, precipitation
Hurricane Melissa

## Slide 6: MicroWave Imager (MWI) & Ice Cloud Imager (ICI)
Channel | Frequency (GHz) | Pol.
MWI-1 | 18.7 | V, H
MWI-2 | 23.8 | V, H
MWI-3 | 31.4 | V, H
MWI-4 | 50.3 | V, H
MWI-5 | 52.7 | V, H
MWI-6 | 53.24 | V, H
MWI-7 | 53.75 | V, H
MWI-8 | 89.0 | V, H
MWI-9 | 118.75033.2 | V
MWI-10 | 118.75032.1 | V
MWI-11 | 118.75031.4 | V
MWI-12 | 118.75031.2 | V
MWI-13 | 165.50.75 | V
MWI-14 | 183.317.0 | V
MWI-15 | 183.316.1 | V
MWI-16 | 183.314.9 | V
MWI-17 | 183.313.4 | V
MWI-18 | 183.312.0 | V
MWI Imaging channels
in the “windows” (18.7, 31.4, 89.0, 165.5 GHz) and low WV absorption (23.8 GHz)
MWI Temperature sounding in the O2 50/60 complex - 118 GHz line
MWI
18 channels (V/H until 89 GHz; V above 89 GHz)
Spatial resolution: 50 km at low freqs., 10 km at high freqs.
Precipitation mission:
18 – 31.4 GHz: wind, ice/snow cover, TCWV (+183 GHz)
50/60 & 118 GHz: light precipitation/snowfall
89 & 165 GHz: Snowfall, precipitation
183 GHz: Snowfall, cloud slicing, WV
Humidity sounding in the 183 GHz line (some of bands in common with ICI)

## Slide 7: MicroWave Imager (MWI) & Ice Cloud Imager (ICI)
Channel | Frequency (GHz) | Pol.
ICI-1 | 183.317.0 | V
ICI-2 | 183.313.4 | V
ICI-3 | 183.312.0 | V
ICI-4 | 243.22.5 | V, H
ICI-5 | 325.159.5 | V
ICI-6 | 325.153.5 | V
ICI-7 | 325.151.5 | V
ICI-8 | 4487.2 | V
ICI-9 | 4483.0 | V
ICI-10 | 4481.4 | V
ICI-11 | 6644.2 | V, H
Channel | Frequency (GHz) | Pol.
MWI-1 | 18.7 | V, H
MWI-2 | 23.8 | V, H
MWI-3 | 31.4 | V, H
MWI-4 | 50.3 | V, H
MWI-5 | 52.7 | V, H
MWI-6 | 53.24 | V, H
MWI-7 | 53.75 | V, H
MWI-8 | 89.0 | V, H
MWI-9 | 118.75033.2 | V
MWI-10 | 118.75032.1 | V
MWI-11 | 118.75031.4 | V
MWI-12 | 118.75031.2 | V
MWI-13 | 165.50.75 | V
MWI-14 | 183.317.0 | V
MWI-15 | 183.316.1 | V
MWI-16 | 183.314.9 | V
MWI-17 | 183.313.4 | V
MWI-18 | 183.312.0 | V
MWI Imaging channels
in the “windows” (18.7, 31.4, 89.0, 165.5 GHz) and low WV absorption (23.8 GHz)
MWI Temperature sounding in the O2 50/60 complex - 118 GHz line
Humidity sounding in the 183 GHz line (some of bands in common with ICI)
..and: ICI channels in “quasi-windows” (243, 664 GHz) and WV bands (325, 448 GHz)
ICI CHANNELS
L1B product
ICI
11 channels (V; 243 & 664 GHz in V/H)
Spatial resolution: 16 km
Cloud ice mission:
183 GHz: Snowfall, cloud slicing, cloud ice, WV
Strong WV bands: ice water content/path, ice sizes
V/H quasi window channels: ice shape and orientation

## Slide 8: CIMR: The Copernicus Imaging Microwave Radiometer
Freq. band | L | C | C | X | K | Ka
Variables | Salinity | Sea surface winds & temp. | Sea surface winds & temp. |  | Water vapour, cloud & rain | 
Frequency [GHz] | 1.4135 | 6.925 | 6.925 | 10.65 | 18.7 | 36.5
Footprint [km] | <60 | ≤15 | ≤15 | ≤15 | ≤5.5 | <5
Polarisation | Full Stokes |  |  |  |  | 
Swath | >1900 km |  |  |  |  | 
Observation Zenith Angle [deg] | 52.0 ±1.0 | 55.0 ±2.0 |  |  |  | 
Objective: High spatial resolution PMW observations with global coverage and sub-daily revisits at poles to address EU polar Arctic policy
Orbit: Sun-synchronous polar at ~830 km
Coverage: 95% globally
8.6 m antenna!
L2 Variable ID | Description | Spatial resolution
SST-O | Sea Surface Temperature | 15 km
SSS-O | Sea Surface Salinity | < 60 km
OWS-O | Ocean Surface Wind Vector |  40 km (g=15km)
PR-A | Precipitation rate | 10 km (g=5 km)
LWP-A | Liquid Water Path | 15 km (g=5 km)
TCWV-A | Total Column Water Vapour | 15 km (g=5 km)
EUMETSAT L2 Ocean and Atmosphere products

## Slide 9: EPS-Sterna constellation
Constellation Architecture
3 Sun-synchronous orbital planes at 595 km altitude.
Nominal constellation: 6 satellites, 2 per orbital plane
Repeat cycle per individual satellite: 9 days.
SmallSat: ~ 135 kg, 11 x 0.7 x 0.8 m
Microwave Radiometer (MWR) Sterna
Across track, with 19 channels (50.3 – 325 GHz)
Swath ~ 2000 km
The Artic Weather Satellite (AWS) is a mission launched by the European Space Agency (ESA) on August 2025 as a demonstrator for the future EPS-Sterna constellation
Channel name | Centre Frequency [GHz] | footprint size [km] | Objective
STERNA-11 | 50.3 | ≤ 40 km (±25%) | Temperature Sounding
STERNA-12 | 52.8 |  | 
STERNA-13 | 53.246 |  | 
STERNA-14 | 53.596 |  | 
STERNA-15 | 54.4 |  | 
STERNA-16 | 54.94 |  | 
STERNA-17 | 55.5 |  | 
STERNA-18 | 57.290344 |  | 
STERNA-21 | 89 | ≤ 20 km (±25%) | Window and Cloud detection
STERNA-31 | 165.5 | ≤ 10 km (±25%) | Window/humidity sounding
STERNA-32 | 176.311 |  | 
 |  |  | Humidity sounding
STERNA-33 | 178.811 |  | 
STERNA-34 | 180.311 |  | 
STERNA-35 | 181.511 |  | 
STERNA-36 | 182.311 |  | 
STERNA-41 | 325.15±1.2 | ≤ 10 km (±25%) | Humidity sounding/cloud detection
STERNA-42 | 325.15±2.4 |  | 
STERNA-43 | 325.15±4.1 |  | 
STERNA-44 | 325.15±6.6 |  | 
Courtesy of ESA
Provides also information on:
Precipitation (liquid/solid)
Weak precipitation
Cloud ice, IWP
EUMETSAT will support the extension of AWS operations from August 2026
Notes: The four Sterna bands have different geolocations

## Slide 10: Precipitation products at a glance
NWC SAF, HSAF, and CM SAF provide complementary products
https://www.nwcsaf.org/
https://hsaf.meteoam.it/
https://www.cmsaf.eu/
… for low-latency nowcasting applications
… for near-real-time hydrological applications
… for long-term Climate Data Records supporting climate monitoring

## Slide 11: Precipitation products at a glance
Hydrology & Water Management SAF precipitation products
LEO PMW:
Surface precipitation from conical scanner (SSMIS)
Surface precipitation from cross-track scanners (MHS, ATMS)
Gridded precipitation from PMW sensors (SSMIS, AMSR-2, GMI, ATMS, AMSU/MHS)
Blended GEO IR-LEO PMW:
Surface precipitation based on SEVIRI and PMW estimates (+ convective precipitation)
Surface precipitation based on FCI and PMW estimates
Other blended:
Gridded daily precipitation by merging soil moisture rainfall with PMW estimates
Future precipitation products | EUMETSAT & SAFs
PMW: Liquid & frozen precipitation from MWI, MWS, Sterna, CIMR (+ high-latitude products)
  Utilization of active sensors (cloud + precipitation radars) & machine learning
  Snowfall retrieval based on AWS/Sterna
Blended GEO IR – LEO PMW:
  FCI & EPS-SG
  Development of global products & SM2RAIN for accumulated precipitation

## Slide 12
Key takeaways
EPS-SG offers new capabilities (channels sensitive to weak liquid/solid precipitation, sub-mm channels)
EPS-Sterna unlocks extended coverage & revisit (channels sensitive to weak liquid/solid precipitation, sub-mm channels)
CIMR unlocks potential synergies at high latitudes (high spatial resolution & crucial information on ice-covered surfaces)
Enhanced precipitation products (new sensors, active observations, ML)
Thank you!
Questions are welcome.