## Slide 1: Validation of GSMaP Using a 1-Minute Precipitation Rate Product (1MPR) Combining Ground-based Radar and Rain Gauge Data over Japan
IPWG 12 (Krakow, Poland), July 7th, 2026
4.3, Session 4 (Product Assessments)
Shinta SETO (Nagasaki University, Japan)
Nobuyuki UTSUMI (Institute of Science Tokyo, Japan)

## Slide 2: Background and Purpose
The development of GSMaP assumes precipitation rate estimates from microwave radiometers (MWRs) as hourly precipitation rates.
For the validation of GSMaP, observed hourly precipitation rates are usually used.
The time scale of precipitation rate estimates from MWRs and their time lag relative to ground surface measurements are not clearly known.
The precipitation rate estimates of GSMaP derived from MWRs are validated with 1-minute precipitation rate product (1MPR) over Japan.

## Slide 3: Reviews on time scale and time lag of rain rate estimates by microwave radiometers
Red: Pacomoke (Pacific Coast, USA)
Blue: WegenerNet (Alps)
Green: Walnut (west of USA)
Tan et al. (2018) analyzed the time lag between GPROF estimates and rain gauge data
  High spatial density of rain gauges
  Time lag between 0 and 30 minutes
Tan et al.(2018;JHM)

## Slide 4: Reviews on time scale and time lag of rain rate estimates by microwave radiometers
You et al. (2019) analyzed the time lag between GPROF and ground-based radar data (MRMS)
  Rainfall : Time lag = 4 minutes
  Snowfall : Time lag = 20 minutes
You et al.(2019;GRL)

## Slide 5: 1-minute precipitation rate product (1MPR)
Over Japan
Spatial resolution=250m, Temporal resolution = 1min
XRAIN (C-band and X-band composite data)
Rain gauges (~1300 by JMA and ~2200 by MLIT)
JMA
Gauges
MLIT
Gauges
XRAIN
Radars

## Slide 6: 1-minute precipitation rate product (1MPR)
With Rain gauges
Without
Rain Gauges
XRAIN
Rain gauge
1MPR
Interpolation
XRAIN
Coefficients
1MPR
Smoothing
Interpolation
Coefficients

## Slide 7: 1-minute precipitation rate product (1MPR)
In the development of 1MPR, the time lag correction with the ground surface has not been implemented for XRAIN.
Correction method with the following assumptions
  Any location is observed by the nearest radar
  The radar elevation angle is always at 1.8 degrees
  Considering XRAIN observation altitude, 1 min. time lag is given for 250 m of altitude. Consequently, the timestamp of 1MPR is delayed.
Surface
radar
altitude
1.8o
Time difference between radar observation and ground measuremetns
1 min 250m

## Slide 8: Validation of GSMaP
<Data>
GSMaP Version 8 standard product
  Rain rate estimates
  Sateinfo (satellite information)
   Only estimates by MWRs are analyzed
  Timeinfo (time stamp)
1MPR
  Averaged for 0.2 degrees.
  Averaged for 1 min, 10 min, 30 min, 60 min.
  With time lag : -30 min to +60 min
60 min average with +30 min lag
Observation
By MWR
+ 30 min
+ 60 min
-60 min
-30 min
-45 min
-15 min
+ 15 min
+ 45 min
GSMaP
1MPR
0.2 deg.
0.1 deg.
Footprint of MWR

## Slide 9: Validation of GSMaP
<Target Period>
Mar, Jun, Sep, Dec of 2022
<Target Area>
XRAIN area excluding Okinawa
Quantitative measurement area
  *60 km from X-band radar or 120 km from C-band radar
<Classification>
Ocean/Land is judged by GLCNMO
  Ocean : 100 % of water surface
  Land : 10 % or lower of water
Over Ocean (quantitative)
Over Land (quantitative)

## Slide 10: Validation of GSMaP
1-min average, lag=0 min
1-min average, lag=15 min
CC = 0.672
CC = 0.715
Over Ocean, AMSR2

## Slide 11: Validation of GSMaP
10-min average, lag=0 min
10-min average, lag=15 min
CC = 0.674
CC = 0.718
Over Ocean, AMSR2

## Slide 12: Validation of GSMaP
30-min average, lag=0 min
30-min average, lag=15 min
CC = 0.689
CC = 0.720
Over Ocean, AMSR2

## Slide 13: Validation of GSMaP
Over Ocean, AMSR2
60-min average, lag=0 min
60-min average, lag=15 min
CC = 0.696
CC = 0.710

## Slide 14: Time scale and time lag of GSMaP
Ocean, AMSR2
CC with different time scale and time lag
0 min.
30 min.
60 min.
-30 min.
Maximum CC (time lag)
1-min ave. 0.716 (+13 min.)
10-min ave. 0.718 (+14 min.)
30-min ave. 0.721 (+13 min.)
60-min ave. 0.710 (+13 min.)
Time Lag = + 13 min.
Maximum CC = 0.721
(Average time = 25 min.)

## Slide 15: Time scale and time lag of GSMaP
Land, AMSR2
CC with different time scale and time lag
0 min.
30 min.
60 min.
-30 min.
Time Lag = + 10 min.
Maximum CC = 0.527
(Average time = 14 min.)
Maximum CC (time lag)
1-min ave. 0.526 (+10 min.)
10-min ave. 0.526 (+10 min.)
30-min ave. 0.525 (+08 min.)
60-min ave. 0.513 (+04 min.)

## Slide 16: Time scale and time lag of GSMaP
Ocean, GMI
CC with different time scale and time lag
0 min.
30 min.
60 min.
-30 min.
Time Lag = + 13 min.
Maximum CC = 0.770
(Average time = 26 min.)
Maximum CC (time lag)
1-min ave. 0.763 (+12 min.)
10-min ave. 0.766 (+13 min.)
30-min ave. 0.770 (+13 min.)
60-min ave. 0.758 (+13 min.)

## Slide 17: Time scale and time lag of GSMaP
Land, GMI
CC with different time scale and time lag
0 min.
30 min.
60 min.
-30 min.
Time Lag = + 12 min.
Maximum CC = 0.607
(Average time = 30 min.)
Maximum CC (time lag)
1-min ave. 0.599 (+11 min.)
10-min ave. 0.602 (+11 min.)
30-min ave. 0.607 (+12 min.)
60-min ave. 0.596 (+12 min.)

## Slide 18: Time scale and time lag of GSMaP
Ocean, SSMIS
CC with different time scale and time lag
0 min.
30 min.
60 min.
-30 min.
Maximum CC (time lag)
1-min ave. 0.564 (-06 min.)
10-min ave. 0.568 (-03 min.)
30-min ave. 0.584 (-01 min.)
60-min ave. 0.601 (-04 min.)
Average time of longer than 60 min. gives better CC

## Slide 19: Time scale and time lag of GSMaP
Land, SSMIS
CC with different time scale and time lag
0 min.
30 min.
60 min.
-30 min.
Maximum CC (time lag)
1-min ave. 0.649 (+08 min.)
10-min ave. 0.652 (+08 min.)
30-min ave. 0.661 (+08 min.)
60-min ave. 0.666 (+07 min.)
Average time of longer than 60 min. gives better CC

## Slide 20: Time scale and time lag of GSMaP
Ocean, Sounders
CC with different time scale and time lag
0 min.
30 min.
60 min.
-30 min.
Maximum CC (time lag)
1-min ave. 0.628 (+14 min.)
10-min ave. 0.633 (+15 min.)
30-min ave. 0.650 (+14 min.)
60-min ave. 0.666 (+14 min.)
Average time of longer than 60 min. gives better CC

## Slide 21: Time scale and time lag of GSMaP
Land, Sounders
CC with different time scale and time lag
0 min.
30 min.
60 min.
-30 min.
Maximum CC (time lag)
1-min ave. 0.541 (+11 min.)
10-min ave. 0.544 (+11 min.)
30-min ave. 0.554 (+11 min.)
60-min ave. 0.562 (+12 min.)
Average time of longer than 60 min. gives better CC

## Slide 22: Time scale and time lag of GSMaP
Lag. (min) | Ocean | Land
AMSR2 | +13 min. | +10 min.
GMI | +13 min. | +12 min.
SSMIS | -04 min. | +07 min.
Sounders | +14 min. | +12 min.
Scale (min) | Ocean | Land
AMSR2 | 25 min. | 14 min.
GMI | 26 min. | 30 min.
SSMIS | > 60 min. | > 60 min.
Sounders | > 60 min. | > 60 min.

## Slide 23
Time lag to ground measurements
  Time lag between 10 min. to 15 min. is derived except for SSMIS
  No clear difference between Ocean and Land
Time scale (average time for maximum CC)
  30 min. or shorter for AMSR2 and GMI
  Over 60 min. for SSMIS and Sounders
Difference of spatial resolutions among sensors and frequencies may affect the results.
  Spatial matchup with 1MPR should be considered more.
Time scale and time lag of GSMaP

## Slide 24: Expected results on time scale and time lag of rain rate estimates by microwave radiometers
Rain from the space 2
Land
scattering algorithm
Sensitive to solid precipitation
Time scale <-> Storm height - 0 oC height
Time lag <-> relative large
Ocean
mainly emission algorithm
Sensitive to liquid precipitation
Time scale <-> 0 oC height
Time lag <-> relatively small

## Slide 25
Time lag to ground measurements
  Time lag between 10 min. to 15 min. is derived except for SSMIS
  No clear difference between Ocean and Land
Time scale (average time for maximum CC)
  30 min. or shorter for AMSR2 and GMI
  Over 60 min. for SSMIS and Sounders
Difference of spatial resolutions among sensors and frequencies may affect the results.
  Spatial matchup with 1MPR should be considered more.
Time scale and time lag of GSMaP

## Slide 26
 | Sensor | Satellite | Spatial resolution
Microwave Imagers | AMSR2 | GCOM-W | 14km×22km (18.7GHz) 3km×5km (89.0GHz)
 | GMI | GPM core | 11km×18km (18.7GHz) 4km×7km (89.0GHz)
 | SSMIS | DMSP (F16,F18) | 43km×69km (19.3GHz) 13km×15km (85.5GHz)
Microwave Sounders | AMSU | NOAA-19 Metop-B Metop-C | 48km (23.8～89GHz) 16km (89～183GHz)
 | ATMS | NPP | 75km (23～32GHz) 32km (50～90GHz) 16km (165～183GHz)
Spatial resolutions of microwave radiometers

## Slide 27: Recommendation for GSMaP
For hourly rain rate estimates for X:00 to (X+1):00 observations between X:00 to (X+1):00 are used.
  Time lag is set to be -30 min to + 30 min.
  Positive time lag over 30 min may give better result than negative time lag under 30 min

## Slide 28: Recommendation for GSMaP
Ocean, AMSR2
Land, AMSR2
+30 to +43 min
-30 to -17 min
+30 to +36 min
-30 to -24 min

## Slide 29: Recommendation for GSMaP
Ocean, GMI
Land, GMI
+30 to +43 min
-30 to -17 min
+30 to +42 min
-30 to -18 min

## Slide 30: Recommendation for GSMaP
Ocean, SSMIS
Land, SSMIS
+30 to +37 min
-30 to -23 min

## Slide 31: Recommendation for GSMaP
Ocean, MWS
Land, MWS
+30 to +44 min
-30 to -16 min
+30 to +41 min
-30 to -19 min

## Slide 32: Recommendation for GSMaP
For hourly rain rate estimates from X:00 to (X+1):00 observations between X:00 to (X+1):00 are used.
  Time lag is set to be -30 min to + 30 min.
  Positive time lag over 30 min may give better result than negative time lag under 30 min
For hourly rain rate estimates from X:00 to (X+1):00, observations in the following time can be used.
 | Ocean | Land
AMSR2 | (X-1):47 to X:47 | (X-1):54 to X:54
GMI | (X-1):47 to X:47 | (X-1):48 to X:48
SSMIS | X:00 to (X+1):00 | (X-1):53 to X:53
MWS | (X-1):46 to X:46 | (X-1):49 to X:49

## Slide 34: Ocean, AMSR2

## Slide 35: Ocean, GMI

## Slide 36: Ocean, SSMIS

## Slide 37: Ocean, MWS

## Slide 38: Land, AMSR2

## Slide 39: Ocean, GMI

## Slide 40: Ocean, SSMIS

## Slide 41: Ocean, MWS

## Slide 42: 1MPRの作成手順
時刻
降水強度
転倒
１回目
転倒
２回目
転倒
３回目
転倒
４回目
XRAINの降水強度
1分

## Slide 43: 1MPRの作成手順
時刻
降水強度
転倒
１回目
転倒
２回目
転倒
３回目
転倒
４回目
降水量
0.2mm
降水量
0.6mm
降水量
0.4mm
XRAINの降水強度

## Slide 44: 1MPRの作成手順
時刻
降水強度
転倒
１回目
転倒
２回目
転倒
３回目
転倒
４回目
降水量
0.5mm
降水量
0.5mm
降水量
0.5mm
補正後の降水強度
XRAINの降水強度
0.2 → 0.5
0.6 → 0.5
0.4 → 0.5
+0.1
×0.83
+0.3
補正

## Slide 45: 1MPRの作成手順
時刻
降水強度
転倒
１回目
転倒
２回目
転倒
３回目
転倒
４回目
降水量
0.5mm
降水量
0.5mm
降水量
0.5mm
補正後の降水強度
XRAINの降水強度
S=1.0
C= 0.3/T1
S=0.833
C=0
S=1.0
C=0.1/T2
S≦1とする
S＜1の場合、C=0
(補正後の降水強度)=S×(XRAINの降水強度)+C

## Slide 46: 1MPRの作成手順
雨量計1
雨量計2
雨量計3
補正係数 S1 ,C1
距離 d1
距離 d2
距離 d3
S0=1 C0=0 D=111.111km
Wは「補正しない」の重み
Nは使用する雨量計の数
格子の補正係数の決定
補正係数 S2 ,C2
補正係数 S3 ,C3
(補正後の降水強度)=S×(XRAINの降水強度)+C