## Slide 1: Deep Learning Radar Nowcasting over the Upper Tyrrhenian Sea
A. Antonini, M. Passeri, F. Fibbi, L. Fibbi, S. Melani, A. Mazza, A. Ortolani

## Slide 2: UPPER TYRRHENIAN CROSS-BORDER RADAR COMPOSITE

## Slide 3
Mont Vial (X-band pol)
Monte Verrugoli (X-band)
Monte Settepani (C-band pol)
Elba (X-band)
Monte Rasu (C-band pol)
Aleria (S-band)
UPPER TYRRHENIAN CROSS-BORDER RADAR COMPOSITE

## Slide 4: UPPER TYRRHENIAN CROSS-BORDER RADAR COMPOSITE
WEATHER RADAR DATA ACQUISITION
DATA HOMOGENEIZATION
DATA FILTERING:
NO DATA
SPECKLE
RADIAL SPIKE
FILTERED REFLECTIVITY RECONSTRUCTION
VERTICAL MAXIMUM INTENSITY
PROJECTION TO A COMMON GRID
RADAR COMPOSITE GENERATION

## Slide 5: UPPER TYRRHENIAN CROSS-BORDER RADAR COMPOSITE
https://geoportale.lamma.rete.toscana.it/radar_mosaico/index.html

## Slide 6: REAL-TIME FILTERING
The filter applies a causal adaptive-background approach, retaining only echoes that exceed both a minimum intensity threshold and a residual threshold relative to the background estimated from previous frames.

## Slide 7: REAL-TIME FILTERING
Adaptive background
Geotiff ingest
Frame filtering comparing with background and min-echo
Morphological and single noise pixels cleaning
Geotiff output

## Slide 8: COMPARED TECHNIQUES
RainNet
DGMR

## Slide 9
Input: last 4 radar frames (I1..I4) in the G generator.
Generator encodes through a stack of convolutional residual blocks that progressively extract multi-scale spatial features.
Z: latent stocastic sampled variable to generate probabilistic prediction (ensemble).
G generates a sequence Ŷ(1:T).
Discriminators:
- Spatial: precipitation morphology, convective structures,
spatial textures on single frames.
Temporal: evaluates the entire predicted sequence, for temporal consistency, dynamic evolution
pixel-wise regularization: the average of the generated samples must approach the true observation (reduces offsets).
https://github.com/pySTEPS/pysteps-dgmr-nowcasts
Ravuri, S., Lenc, K., Willson, M. et al. Skilful precipitation nowcasting using deep generative models of radar. Nature 597, 672–677 (2021)
DGMR

## Slide 10
TILING
Image subdivision into partially overlapping (64-pixel) 256x256 patches
Normalization of each patch to the [0, 1] range
Inference performed on each patch using 4 consecutive images
Image reconstruction (overlap-add method) ensuring spatial coherence
DGMR

## Slide 11
CNN encoder–decoder inspired by U-Net/SegNet for +5-minute nowcasting; it uses four scans (at t−15, t−10, t−5, and t) as input and precipitation at t+5 minutes as the target. Values ​​are transformed using log(x + 0.01).
The model was trained on the DWD RADOLAN RY product (rainfall accumulation: 1 km / 5 min) rather than reflectivity; therefore, if starting from dBZ, a conversion sequence (Z–R → mm/h → mm/5min) is required prior to the log-transformation.
It is implemented in Keras (Functional API): https://github.com/hydrogo/rainnet
Pre-trained weights and the model are available on Zenodo [rainnet_weights.h5].
RAINNET

## Slide 12
Marshall-Palmer z-R Relationship
RAINNET

## Slide 13
Structural Similarity Index (SSIM)
Given two images x and y, the SSIM is computed through the standard formula (Wang et al., 2004)
where:
𝜇𝑥 ,𝜇𝑦 = average of 𝑥 and 𝑦
𝜎𝑥2, 𝜎𝑦2 = variance of 𝑥 and 𝑦
σxy = cvariance
𝐶1, 𝐶2 C1,C2 = stabilization constants
SSIM is typically in [0,1]
Mean Squared Error (MSE)
Given two fields e over N valid pixels:
EVALUATION METRICS
• Similarity of spatial patterns, texture and contrast • Sensitive to morphology of precipitation systems • Range: typically 0–1; higher is better
• Average squared pixel-wise error • Strongly penalizes large intensity errors • Lower is better; units are squared field units
Luminance (L): Compares the average brightness of the two images.
Contrast (C): Compares the variance (distribution) of pixel intensities.
Structure (S): Compares the correlation between local pixel patterns

## Slide 14
CASE STUDY 20/8/2025

## Slide 15
CASE STUDY 20/8/2025
T0+60 min
T0+30 min

## Slide 16
CASE STUDY 20/8/2025

## Slide 17
CASE STUDY 28/8/2025

## Slide 18
CASE STUDY 28/8/2025

## Slide 19
CASE STUDY 28/8/2025

## Slide 20
CASE STUDY 20/10/2025

## Slide 21
CASE STUDY 20/10/2025
T0+60 min
T0+30 min
T0+45 min

## Slide 22
CASE STUDY 20/10/2025

## Slide 23
CASE STUDY 13/4/2026

## Slide 24
CASE STUDY 13/4/2026
T0+60 min
T0+30 min
T0+45 min

## Slide 25
CASE STUDY 13/4/2026

## Slide 26
INTRODUCTION OF ANCILLARY DATA

## Slide 27
Implementation of nowcasting algorithms (DGMR and RainNet)
Preliminary validation using selected case studies demonstrates potential that complements optical flow algorithms for convective phenomena.
Main limitation relates to processing time (5–10 minutes using Colab environment).
Future integration with other sensors (satellites, lightning detection, ground-based measurements, GNSS-meteo) for a better dynamic interpretation of the phenomena.
CONCLUSIONS AND FUTURE WORKS